FIREWALL&DMZ

I. Introduce
  Firewall is a network security system, can be based on hardware or software, using rules to control traffic entering and leaving the system. A firewall acts as a barrier between a secure network and an insecure network. It controls access to network resources through an active control model. That is, only traffic that conforms to the policy defined in the firewall can access the network, all other traffic is rejected.
  DMZ is a word very commonly used in military zones and the computer field. DMZ stands for Demilitarized Zone. Understood as the demilitarized zone, military frontier, or demilitarized zone. Areas with no military activity took place, so this was also where peaceful urban areas were away from gang territories. However, DMZ is also an acronym used in informatics. In computing a DMZ is a networked device (range of networked devices or subnets), for example a computer, placed outside of a firewall or other security measures on the network.
Purpose of DMZ:
  In computer security, for the small and medium networks, we setup a firewall that processes all the requests from the internal network (LAN) to the Internet, and from the Internet to the LAN.
  This firewall is the only protection the internal network has in these setups; it handles any NAT (Network Address Translation), by forwarding and filtering requests as its configuration.
  For small companies, this is usually a good choice. But for the large system, putting all servers behind a firewall is poor security.
  That’s why perimeter security networks (also called demilitarized zone networks or DMZs) are used to separate the internal network from the outside world. This way, outsiders can access the public information in the DMZ, while the private, proprietary information is kept safely behind the DMZ, into the internal network.
  Here are a few examples of services that you can keep in the Demilitarized Zone Network:
- webservers with public information
- the front-end of your application (the back-end should be kept safely behind the DMZ)
- mail server
- authentication services
- services like HTTP for general public usage, secure SMTP, secure FTP, and secure Telnet
- VoIP servers
- VPN endpoints
- application gateways
- test and staging servers
  The DMZ Network exists to secure the hosts (internal network) from most vulnerable to attack. These hosts usually involve services that extend to users outside of the local area network, the most common examples being email, web servers, and DNS servers. Because of the increased potential for attack, they are placed into the monitored subnetwork to help protect the rest of the network if they become compromised.

II. Construction architecture of DMZ&Firewall
The basic components that make up the DMZ are: IP addresses and firewalls.
Two important identifiers of the DMZ:
- It has a different network ID than the internal network.
- It is separated from the Internet and the internal network by the firewall(s).

1. IP addresses in DMZ:
  DMZ can use public IP or private IP for servers depending on the configuration on the firewall and the DMZ structure.
  When we use a public IP for the DMZ, you will need to subnet the block of IP addresses that ISP gives us to get two separate network IDs. Then one network ID is used for the external interface (network card directly connected to the ISP) of the firewall and the other network ID is used for the DMZ network. However, remember when subnet this public IP block, must configure router so that packets from outside Internet can reach the DMZ.
  We can also create a DMZ with the same network ID as the internal network by using VLAN Tagging (IEEE 802.1q) while ensuring the DMZ and the internal network are separation. In this case, the servers in the DMZ and the workstations on the internal network are all plugged into a switch (or different switches but these switches are connected together) and assigned to the different VLANs.
In case using private IP for the DMZ, need NAT (some firewalls already support this feature) to convert these private IPs to a public IP (which is assigned to the external interface of the firewall between the Internet and the DMZ).

2. DMZ models
 a. components:
First, we need to learn about the components in the secure network model, the components in the network model include:
- Local area network(LAN): the place where network devices, workstations and servers belong to the internal network of the unit.
- DMZ zone: a neutral network zone between the internal network and the Internet, which contains information allowing users from the Internet to access and accept risks from Internet attacks. Services commonly deployed in the DMZ are: Web server, Mail server, DNS server, FTP server, ... - Server Farm: the place where servers don’t directly provide services to the Internet. Usually to deploy Database Server, LDAP Server, …
- Internet: Also known as external network, connects to the global Internet. The security network model organization to ensure security has a great impact on the safety of network systems and other Web portal. This is the first base for the construction of defense and protection systems. In addition, the organization of a secure network model can effectively limit internal and external attacks.

 b. Models:
  In this model, the Internet area, intranet area, and DMZ area are designed separately. In addition, we put a firewall between network zones to control the flow of information between network zones and protect the network areas from unauthorized attacks.

  Put a firewall between the Internet area and the DMZ area and a firewall between the DMZ area and the internal network area.

 Put a firewall between the Internet area and the DMZ network area, a firewall between the DMZ area and the internal network area, and a firewall between the internal network area and the Internet zone. Thus, each access between regions is controlled by a firewall as shown in the figure.

III. How to configure a DMZ area
For example, I use the CISCO ASA to configure a single firewall DMZ.

## Lab topology setup

Step 1.  Cấu hình thông tin trên các cổng của FW:
Cổng Inside
interface GigabitEthernet0/0 nameif inside security-level 100 ip address 192.168.0.1 255.255.255.0

Cổng DMZ
interface GigabitEthernet0/1 nameif DMZ security-level 50 ip address 192.168.10.1 255.255.255.0

Cổng Outside
interface GigabitEthernet0/2 nameif outside security-level 0 ip address dhcp setroute //Tự động chèn route default vào bảng định tuyến sau khi nhận được địa chỉ IP

2. Cấu hình định tuyến:
Cấu hình default-route trên router Core. Cấu hình static route trên FW với câu lệnh:

route inside 192.168.2.0 255.255.255.0 192.168.0.254

Cấu hình hoàn thành bước này bạn có thể truy cập thành công dịch vụ DMZ từ vùng Inside.

Lưu ý: Mặc định ASA không cho phép ICMP qua giữa các vùng, để kiểm tra Ping từ vùng Inside bạn cần cấu hình thêm:

ciscoasa(config)# policy-map global_policy ciscoasa(config-pmap)# class inspection_default ciscoasa(config-pmap-c)# inspect icmp

3.  Cấu hình SSH trên Firewall ASA:

ciscoasa(config)# username waren password waren ciscoasa(config)# crypto key generate rsa general-keys WARNING: You have a RSA keypair already defined named Do you really want to replace them? [yes/no]: y Keypair generation process begin. Please wait... ciscoasa(config)# ssh 192.168.2.10 255.255.255.255 inside ciscoasa(config)# ssh version 2 ciscoasa(config)# aaa authentication ssh console LOCAL

Sau khi hoàn thành bước này bạn có thể truy cập SSH từ PC (192.168.1.10):

4.  Cấu hình Staic NAT và ACL để cho từ bên ngoài có thể truy cập dịch vụ remote desktop vùng DMZ:
B1: Cấu hình Object Network:
object network DMZ_10.10 host 192.168.10.10

B2: Cấu hình Object Service:
object service RDP service tcp source eq 3389

B3: Cấu hình NAT:
nat (inside,outside) source static DMZ_10.10 interface service RDP RDP

B4: Cấu hình ACL để cho phép truy cập từ outside vào DMZ:
access-list POLICY extended permit tcp any host 192.168.10.10 eq 3389 access-group POLICY in interface outside

Sau khi cấu hình hoàn thành bước này bạn sẽ có thể truy cập được dịch vụ Remote Desktop từ vùng Outside (lưu ý: 192.168.1.67 là địa chỉ của cổng outside trong trường hợp này):
5. Cấu hình PAT để cho phép người dùng từ Inside có thể truy cập được Internet:

B1: Cấu hình Object:
object network USER subnet 192.168.2.0 255.255.255.0

B2. Cấu hình PAT:
nat (inside,outside) source dynamic USER interface // Địa chỉ của người dùng được NAT ra địa chỉ của interface outside.

Sau khi cấu hình hoàn thành bước này bạn sẽ có thể truy cập được Internet

REFERRENCES:
https://www.speaknetworks.com/cisco-asa-dmz-configuration-example/