FIREWALL&DMZ

I. Introduce
  Firewall is a network security system, can be based on hardware or software, using rules to control traffic entering and leaving the system. A firewall acts as a barrier between a secure network and an insecure network. It controls access to network resources through an active control model. That is, only traffic that conforms to the policy defined in the firewall can access the network, all other traffic is rejected.
  DMZ is a word very commonly used in military zones and the computer field. DMZ stands for Demilitarized Zone. Understood as the demilitarized zone, military frontier, or demilitarized zone. Areas with no military activity took place, so this was also where peaceful urban areas were away from gang territories. However, DMZ is also an acronym used in informatics. In computing a DMZ is a networked device (range of networked devices or subnets), for example a computer, placed outside of a firewall or other security measures on the network.

II. Construction architecture of DMZ&Firewall
The basic components that make up the DMZ are: IP addresses and firewalls.
Two important identifiers of the DMZ:
- It has a different network ID than the internal network.
- It is separated from the Internet and the internal network by the firewall(s).

1. IP addresses in DMZ:
  DMZ can use public IP or private IP for servers depending on the configuration on the firewall and the DMZ structure.
  When we use a public IP for the DMZ, you will need to subnet the block of IP addresses that ISP gives us to get two separate network IDs. Then one network ID is used for the external interface (network card directly connected to the ISP) of the firewall and the other network ID is used for the DMZ network. However, remember when subnet this public IP block, must configure router so that packets from outside Internet can reach the DMZ.
  We can also create a DMZ with the same network ID as the internal network by using VLAN Tagging (IEEE 802.1q) while ensuring the DMZ and the internal network are separation. In this case, the servers in the DMZ and the workstations on the internal network are all plugged into a switch (or different switches but these switches are connected together) and assigned to the different VLANs.
In case using private IP for the DMZ, need NAT (some firewalls already support this feature) to convert these private IPs to a public IP (which is assigned to the external interface of the firewall between the Internet and the DMZ).

2. DMZ models
 a. components:
First, we need to learn about the components in the secure network model, the components in the network model include:
- Local area network(LAN): the place where network devices, workstations and servers belong to the internal network of the unit.
- DMZ zone: a neutral network zone between the internal network and the Internet, which contains information allowing users from the Internet to access and accept risks from Internet attacks. Services commonly deployed in the DMZ are: Web server, Mail server, DNS server, FTP server, ... - Server Farm: the place where servers don’t directly provide services to the Internet. Usually to deploy Database Server, LDAP Server, …
- Internet: Also known as external network, connects to the global Internet. The security network model organization to ensure security has a great impact on the safety of network systems and other Web portal. This is the first base for the construction of defense and protection systems. In addition, the organization of a secure network model can effectively limit internal and external attacks.

 b. Models:
  In this model, the Internet area, intranet area, and DMZ area are designed separately. In addition, we put a firewall between network zones to control the flow of information between network zones and protect the network areas from unauthorized attacks.

  Put a firewall between the Internet area and the DMZ area and a firewall between the DMZ area and the internal network area.

  Put a firewall between the Internet area and the DMZ network area, a firewall between the DMZ area and the internal network area, and a firewall between the internal network area and the Internet zone. Thus, each access between regions is controlled by a firewall as shown in the figure.